## Slide 1: Cache Optimization Summary
Technique | MR | MP | HT | Complexity
Larger Block Size | + | - |  | 0
Higher Associativity | + |  | - | 1
Victim Caches | + |  |  | 2
Pseudo-Associative Caches | + |  |  | 2
HW Prefetching of Instr/Data | + | + |  | 2
Compiler Controlled Prefetching | + | + |  | 3
Compiler Reduce Misses |  |  |  | 0
Priority to Read Misses |  | + |  | 1
Early Restart & Critical Word 1st |  | + |  | 2
Non-Blocking Caches |  | + |  | 3
Second Level Caches |  | + |  | 2
Better memory system |  | + |  | 3
Small & Simple Caches | - |  | + | 0
Avoiding Address Translation |  |  | + | 2
Pipelining Caches |  |  | + | 2
Intro
Four Q?
Cache Performance
Cache Optimizations
Virtual Memory

## Slide 2: Comparing the 2 levels of hierarchy
Parameter | L1 Cache | Virtual Memory
Block/Page | 16B – 128B | 4KB – 64KB
Hit time | 1 – 3 cc | 100 – 200 cc
Miss Penalty (Access time) (Transfer time) | 8 – 200 cc 6 – 160 cc 2 – 40 cc | 1M – 10M cc (Page Fault ) 800K – 8M cc 200K – 2M cc
Miss Rate | 0.1 – 10% | 0.00001 – 0.001%
Placement: | DM or N-way SA | Fully associative (OS allows pages to be placed anywhere in main memory)
Address Mapping | 25-45 bit physical address to 14-20 bit cache address | 32-64 bit virtual address to 25-45 bit physical address
Replacement: | LRU or Random (HW cntr.) | LRU (SW controlled)
Write Policy | WB or WT | WB
Intro
Four Q?
Cache Performance
Cache Optimizations
Virtual Memory

## Slide 3: Paging vs. Segmentation: Pros and Cons
 | Page | Segment
Words per address | One | Two (segment + offset)
Programmer visible? | Invisible to AP | May be visible to AP
Replacing a block | Trivial (all blocks are the same size) | Hard (must find contiguous, variable-size unused portion
Memory use inefficiency | Internal fragmentation (unused portion of page) | External fragmentation (unused pieces of main memory)
Efficient disk traffic | Yes (adjust page size to balance access time and transfer time) | Not always (small segments transfer few bytes)
Intro
Four Q?
Cache Performance
Cache Optimizations
Virtual Memory

## Slide 4: Typical TLB Format
Tag: Portion of virtual address
Data: Physical Page number
Dirty: since use write back, need to know whether or not to write page to disk when replaced
Ref: Used to help calculate LRU on replacement
Valid: Entry is valid
Access rights: R (read permission), W (write perm.)
Virtual Addr. | Physical Addr. | Dirty | Ref | Valid | Access Rights
Intro
Four Q?
Cache Performance
Cache Optimizations
Virtual Memory

## Slide 5: Techniques to exploit parallelism
Technique (Section in the textbook) | Reduces
Forwarding and bypassing | Data hazard (DH) stalls
Delayed branches | Control hazard stalls
Basic dynamic scheduling | DH stalls (RAW)
Dynamic scheduling with register renaming | WAR and WAW stalls
Dynamic branch prediction | CH stalls
Issuing multiple instruction per cycle | Ideal CPI
Speculation | Data and control stalls
Dynamic memory disambiguation | RAW stalls w. memory
Loop Unrolling | CH stalls
Basic compiler pipeline scheduling | DH stalls
Compiler dependence analysis | Ideal CPI, DH stalls
Software pipelining and trace scheduling | Ideal CPI and DH stalls
Compiler speculation | Ideal CPI, and D/CH stalls
ILP
Scoreboard
Tomasulo

## Slide 6: Execution in Dual-issue Tomasulo Pipeline
Iter. | Inst. | Issue | Exe. (begins) | Mem. Access | Write at CDB | Com.
1 | LD.D F0,0(R1) | 1 | 2 | 3 | 4 | first issue
1 | ADD.D F4,F0,F2 | 1 | 5 |  | 8 | Wait for LD.D
1 | S.D 0(R1), F4 | 2 | 3 | 9 |  | Wait for ADD.D
1 | DADDIU R1,R1,-#8 | 2 | 4 |  | 5 | Wait for ALU
1 | BNE R1,R2,Loop | 3 | 6 |  |  | Wait for DAIDU
2 | LD.D F0,0(R1) | 4 | 7 | 8 | 9 | Wait for BNE
2 | ADD.D F4,F0,F2 | 4 | 10 |  | 13 | Wait for LD.D
2 | S.D 0(R1), F4 | 5 | 8 | 14 |  | Wait for ADD.D
2 | DADDIU R1,R1,-#8 | 5 | 9 |  | 10 | Wait for ALU
2 | BNE R1,R2,Loop | 6 | 11 |  |  | Wait for DAIDU
3 | LD.D F0,0(R1) | 7 | 12 | 13 | 14 | Wait for BNE
3 | ADD.D F4,F0,F2 | 7 | 15 |  | 18 | Wait for LD.D
3 | S.D 0(R1), F4 | 8 | 13 | 19 |  | Wait for ADD.D
3 | DADDIU R1,R1,-#8 | 8 | 14 |  | 15 | Wait for ALU
3 | BNE R1,R2,Loop | 9 | 16 |  |  | Wait for DAIDU
ILP
Scoreboard
Tomasulo

## Slide 7: Four Steps of Speculative Tomasulo Algorithm
1. Issue—get instruction from FP Op Queue
  If reservation station and reorder buffer slot free, issue instr & send operands & reorder buffer no. for destination (this stage sometimes called “dispatch”)
2. Execution—operate on operands (EX)
  When both operands ready then execute; if not ready, watch CDB for result; when both in reservation station, execute; checks RAW (sometimes called “issue”)
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting FUs & reorder buffer; mark reservation station available.
4. Commit—update register with reorder result
  When instr. at head of reorder buffer & result present, update register with result (or store to memory) and remove instr from reorder buffer. Mispredicted branch flushes reorder buffer (sometimes called “graduation”)
ILP
Scoreboard
Tomasulo